Project: Kinematics Pick & Place

Here I will consider the rubric points individually and describe how I addressed each point in my implementation.

# Kinematic Analysis
1. Run the forward_kinematics demo and evaluate the kr210.urdf.xacro file to perform kinematic analysis of Kuka KR210 robot and derive its DH parameters.

Analyzing the axes pose and the kr210.urdf.xacro file, I was able to determine the coordinate frames for each joint as seen in the figure.

From here, I could derive the DH parameter table where most of the parameters came directly from .xacro file, but some of them were calculated as follow:

d1 = 0.33 + 0.42 = 0.75

d4 = 0.96 + 0.54 = 1.5

d7 = dG = 0.193 + 0.11 = 0.303

therefore, the DH parameter table is the following:

Links	%alpha_{i-1}	a_{ i-1 }	d_{ i-1 }	%theta_i
0 → 1	0	0	0.75	q1
1 → 2	-%pi/2	0.35	0	-%pi/2 + q2
2 → 3	0	1.25	0	q3
3 → 4	-%pi/2	-0.054	1.5	q4
4 → 5	%pi/2	0	0	q5
5 → 6	-%pi/2	0	0	q6
6 → EE	0	0	0.303	0

2. Transformation matrices

I wrote the transformation matrix from i-1 to i independently in the code and then substitute the parameter value.

    T0_1 = Matrix([[ cos(q1), -sin(q1), 0, a0],
        [ sin(q1)*cos(alpha0), cos(q1)*cos(alpha0), -sin(alpha0), -sin(alpha0)*d1],
        [ sin(q1)*sin(alpha0), cos(q1)*sin(alpha0), cos(alpha0), cos(alpha0)*d1],
        [ 0, 0, 0, 1]])
    T0_1 = T0_1.subs(s)

then I made the composition of homogeneous transformation matrices in order to obtain the complete homogeneous transformation matrix from frame 0 to the EE

    # Composition of Homogeneous Transformation matrix
    T0_2 = T0_1 * T1_2 # base_link to link_2
    T0_3 = T0_2 * T2_3 # base_link to link_3
    T0_4 = T0_3 * T3_4 # base_link to link_4
    T0_5 = T0_4 * T4_5 # base_link to link_5
    T0_6 = T0_5 * T5_6 # base_link to link_6
    T0_G = T0_6 * T6_G # base_link to gripper

but the orientation of the gripper frame in the DH convention is different from what we extract from the .xacro file, so we need to make a couple of rotations of our frame in order to obtain the same orientation. First 180º around the Z axe, and then -90º around the Y axe.

    # Gripper orientation correction
    R_z = Matrix([[ cos(np.pi), -sin(np.pi), 0, 0],
        [ sin(np.pi), cos(np.pi), 0, 0],
        [ 0, 0, 1, 0],
        [ 0, 0, 0, 1]])
    R_y = Matrix([[ cos(-np.pi/2), 0, sin(-np.pi/2), 0],
        [ 0, 1, 0, 0],
        [-sin(-np.pi/2), 0, cos(-np.pi/2), 0],
        [ 0, 0, 0, 1]])
    R_corr = R_z * R_y
so the total homogeneous transformation matrix is:

    # Total homogeneous transform
    T_total = T0_G * R_corr

# 3. Inverse Kinematics

As the robotic arm has six dof and has a spherical joint for the gripper, we can decouple the IK problem in inverse position and inverse orientation.

## 3.1 Inverse Position

For the IP, first we need to calculate the wrist center, having the desired position of the EE relative to frame 0 0_{bold r EE/0} , and the vector from the WC to the EE 0_{bold r EE/WC} , we can calculate the WC position relative to the frame 0 as:

0_{bold r WC/0} = 0_{bold r EE/0} - 0_{bold r EE/WC}

Due to I considered the gripper frame correction in the FK, the vector 0_{bold r EE/WC} is the rotation of the vector [d, 0, 0], therefore:

0_{bold {r} WC/0 } = 0_{bold {r} EE/0 } - d_7 cdot binom{0}{6}R left[ stack{1 # 0 # 0} right ]=left[ stack{p_x # p_y #p_z} right ] - d_7 cdot binom{0}{6}R left[ stack{1 # 0 # 0} right ]

where binom{0}{6}R correspond to a composition of rotations using Euler angles. The convention used is the x-y-z extrinsic rotations, then:

Rrpy = Rot( Z, yaw ) cdot Rot( Y, pitch ) cdot Rot( X, roll )

so having the WC it's easy to obtain %theta_1 :

%theta_1 = arctan(w_y over w_x )

Now for calculating theta 2 and theta 3, we have the following diagram:

Using geometry, trigonometric and cosine law, we can calculate the angles in steps:

r = sqrt{wc_x^2+wc_y^2}-a_1 newline h = wc_z-d_1 newline A = sqrt{ d_4^2+a_3^2 } newline B = sqrt{r^2+h^2} newline %alpha ' = arctan( h over r ) newline %alpha = arccos( {a_2+B^2-A^2} over {2 a_2 B} ) newline %theta_2 = %pi over 2 - %alpha - %alpha ' newline %omega = arctan( a_3 over d_4 ) newline %beta = arccos( {A^2+a_2^2-B^2} over {2 A a_2} )newline %theta_3 = %pi over 2 -%beta-%omega

where a_i and d_i are parameters from the DH table.

## 3.1 Inverse Orientation

For the IO problem, I based my code in the analysis of the IK for the kuka KR210, so I just needed to solve:
R_{3-6} = R_{0-3}^-1 cdot Rypr

using the FK, I could compute R_{0-3}^-1 in terms of q1, q2 and q3 and use it in the code:

        inv_R0_3 = Matrix([[ sin(q2 + q3) * cos(q1), sin(q1) * sin(q2 + q3), cos(q2 + q3)],
        [ cos(q1) * cos(q2 + q3), sin(q1) * cos(q2 + q3), -sin(q2 + q3)],
        [ -sin(q1), cos(q1), 0]])

and R_{ 3-6 } in the same way:
        R3_6 = Matrix([[ -sin(q5)*cos(q4), sin(q4)*cos(q6) + sin(q6)*cos(q4)*cos(q5), -sin(q4)*sin(q6) + cos(q4)*cos(q5)*cos(q6)],
      [ cos(q5), sin(q6), sin(q5)*cos(q6)],
        [ sin(q4)*sin(q5), -sin(q4)*sin(q6)*cos(q5) + cos(q4)*cos(q6), -sin(q4)*cos(q5)*cos(q6) - sin(q6)*cos(q4)]])

from here, I could obtain %theta_4 , %theta_5 y %theta_6 :

%theta_4 = arctan( r_31 over -r_11 ) newline %theta_5 = arctan( sqrt(r_11^2+r_31^2) over r_21 ) newline %theta_6 = arctan( {r_22 sqrt(r_11^2+r_31^2)} over r_23 )

# 4. Code implementation

The code is basically the implementation of the previous analysis of the FK and IK.
All the forward kinematics was implemented in a function outside the CalculateIK service, in order to just do it once at the beginning of execution.
The total transformation matrix was stored in a global variable to use it later for error calculation.
Also, as I mention before, I calculated the inverse of the rotation matrix from frame 0 to frame 3, inv_R0_3, and the rotation matrix between frame 3 and frame 6, R3_6, for use it in the IK solver. It’s worth to notice that this rotation matrix includes the EE frame correction.
After some test of the code, I realized that the gripper was doing a lot of rotations, but the path was OK. The problem is that the function atan2 gives angles between [ -%pi, %pi ] so when the calculated angle is less than %pi , let say %pi - %delta with 0<%delta <%pi/2 , and the next desired angle is greater than %pi , the result from atan2 is a negative angle, so the joint is forced to rotate in the other direction instead of doing the shortest path. In order to get rid of this, I implemented the following code (in this case, for %theta_4 ):

        if (theta4 - theta4_prev) > np.pi:
        theta4 = theta4 - 2 * np.pi
        elif (theta4 - theta4_prev) < -np.pi:
        theta4 = theta4 + 2 * np.pi

where theta4_prev is the previous value of theta4. Together with that, I had to implement the limits for the joints:

if theta4 > 6.109:
        theta4 = theta4 - 2 * np.pi
        elif theta4 < -6.109:
        theta4 = theta4 + 2 * np.pi

where the limits were extracted from the URDF.